## Slide 1: Computer Networks Routing
Lecture 9
Adrian Sergiu DARABANT

## Slide 2: Routing tables (static)
Destination | Gateway | Genmask | Flags | Metric | Ref | Use | Iface
172.16.25.1 | 172.30.0.4 | 255.255.255.255 | UGH | 0 | 0 | 0 | Eth1
193.226.40.128 | 0.0.0.0 | 255.255.255.224 | U | 0 | 0 |  | Eth0
193.0.225.0 | 0.0.0.0 | 255.255.255.0 | U | 0 | 0 |  | Eth0
193.231.20.0 | 0.0.0.0 | 255.255.255.0 | U | 0 | 0 |  | Eth0
172.30.0.0 | 0.0.0.0 | 255.255.0.0 | U | 0 | 0 |  | Eth1
169.254.0.0 | 0.0.0.0 | 255.255.0.0 | U | 0 | 0 |  | Eth1
0.0.0.0 | 193.0.225.9 | 0.0.0.0 | UG | 0 | 0 |  | Eth0
The route command – (Windows/Linux/other OS)

## Slide 3: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 4: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or inversely related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 5: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time

## Slide 6: Distance vector algorithm
Based on Bellman-Ford (BF) equation (dynamic programming):
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 7: RIP-Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 8: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 9: Distance Table: example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
D (A,D)
E
c(E,D) + min {D (A,w)}
D
w
=
=
2+3 = 5
D (A,B)
E
c(E,B) + min {D (A,w)}
B
w
=
=
8+6 = 14
loop!
loop!

## Slide 10: Distance table gives routing table
Distance table
Routing table
A | Next Hop | Dist
B | - | 7
C | - | ∞
D | - | ∞
E | - | 1
B | Next Hop | Dist
A | - | 7
C | - | 1
D | - | ∞
E | - | 8
C | Next Hop | Dist
A | - | ∞
B | - | 1
D | - | 2
E | - | ∞
D | Next Hop | Dist
A | - | ∞
B | - | ∞
C | - | 2
E | - | 2
E | Next Hop | Dist
A | - | 1
B | - | 8
C | - | ∞
D | - | 2
A | Next Hop | Dist
B | - | 7
C | B | 8
D | E | 3
E | - | 1
B | Next Hop | Dist
A | - | 7
C | - | 1
D | C | 3
E | - | 8
C | Next Hop | Dist
A | B | 8
B | - | 1
D | - | 2
E | D | 4
D | Next Hop | Dist
A | E | 3
B | C | 3
C | - | 2
E | - | 2
E | Next Hop | Dist
A | - | 1
B | - | 8
C | D | 4
D | - | 2

## Slide 11: Distance Vector routing
A
E
D
C
B
7
8
1
2
1
2
A | Next Hop | Dist
B | - | 7
C | E | 5
D | E | 3
E | - | 1
B | Next Hop | Dist
A | - | 7
C | - | 1
D | C | 3
E | C | 5
C | Next Hop | Dist
A | D | 5
B | - | 1
D | - | 2
E | D | 4
D | Next Hop | Dist
A | E | 3
B | C | 3
C | - | 2
E | - | 2
E | Next Hop | Dist
A | - | 1
B | D | 5
C | D | 4
D | - | 2
A | Next Hop | Dist
B | E | 6
C | E | 5
D | E | 3
E | - | 1
B | Next Hop | Dist
A | C | 6
C | - | 1
D | C | 3
E | C | 5
C | Next Hop | Dist
A | D | 5
B | - | 1
D | - | 2
E | D | 4
D | Next Hop | Dist
A | E | 3
B | C | 3
C | - | 2
E | - | 2
E | Next Hop | Dist
A | - | 1
B | D | 5
C | D | 4
D | - | 2

## Slide 12: Distance Vector
A | Next Hop | Dist
B | E | 6
C | E | 5
D | E | 3
E | - | 1
B | Next Hop | Dist
A | C | 6
C | - | 1
D | C | 3
E | C | 5
C | Next Hop | Dist
A | D | 5
B | - | 1
D | - | 2
E | D | 4
D | Next Hop | Dist
A | E | 3
B | C | 3
C | - | 2
E | - | 2
E | Next Hop | Dist
A | - | 1
B | D | 5
C | D | 4
D | - | 2
A
E
D
C
B
7
8
1
2
1
2

## Slide 13: Count to Infinity & Solution ?
Good news travels fast
Bad news is slow
Count to infinity !
  Poison reverse
  Split Horizon

## Slide 14: Distance Vector Algorithm:
1 Initialization:
2 for all adjacent nodes v:
3 D (*,v) = infinity /* the * operator means "for all rows" */
4 D (v,v) = c(X,v)
5 for all destinations, y
6 send min D (y,w) to each neighbor /* w over all X's neighbors */
X
X
X
w
At all nodes, X:

## Slide 15: Distance Vector Algorithm (cont.):
8 loop
9 wait (until I see a link cost change to neighbor V
10 or until I receive update from neighbor V)
11
12 if (c(X,V) changes by d)
13 /* change cost to all dest's via neighbor v by d */
14 /* note: d could be positive or negative */
15 for all destinations y: D (y,V) = D (y,V) + d
16
17 else if (update received from V wrt destination Y)
18 /* shortest path from V to some Y has changed */
19 /* V has sent a new value for its min DV(Y,w) */
20 /* call this received new value is "newval" */
21 for the single destination y: D (Y,V) = c(X,V) + newval
22
23 if we have a new min D (Y,w)for any destination Y
24 send new value of min D (Y,w) to all neighbors
25
26 forever
w
X
X
X
X
X
w
w

## Slide 16: Distance Vector Algorithm: example
X
Z
1
2
7
Y

## Slide 17: Distance Vector Algorithm: example
X
Z
1
2
7
Y
D (Y,Z)
X
c(X,Z) + min {D (Y,w)}
w
=
=
7+1 = 8
Z
D (Z,Y)
X
c(X,Y) + min {D (Z,w)}
w
=
=
2+1 = 3
Y

## Slide 18: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates distance table (line 15)
if cost change in least cost path, notify neighbors (lines 23,24)
X
Z
1
4
50
Y
1
algorithm
terminates
“good
news
travels
fast”

## Slide 19: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 20: Distance Vector: poisoned reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 21: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent each
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 22: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 23: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 24: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 25: Inter-AS routing: a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?

## Slide 26: Inter-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
  no longer that widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 27: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)

## Slide 28: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 29: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 30: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 31: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 32: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 33: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 34: BGP path advertisement (more)
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 35: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 36: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 37: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 38: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance

## Slide 39: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 40: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w

## Slide 41: BGP: achieving policy via advertisements (more)
B
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network

## Slide 42: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria